## Slide 1: OCN 479-001
Sensor communications
(Wired edition)

## Slide 2: Today’s topics
Sensor Communications: (Wired edition)

## Slide 3: Sensor Communications
How do we transmit information from some device (a peripheral) to the core microcontroller or computer?

## Slide 4: Analog vs. Digital
Analog
Typically a current (4–20 mA) or voltage (0–3.3 V)
Often proportional to quantity of interest: e.g., T = (100 ºC/3.3 V)*Voltage
Can be other equations: famous one in oceanography is Steinhart–Hart Equation
https://www.electricaltechnology.org/2021/11/thermistor.html

## Slide 5: Steinhart–Hart Equation
A thermistor is a resistor that changes resistance based on temperature
Have known voltage drop across resistor; measure current; calculate resistance
Plug resistance into SHE: 1/T = A + B[ln(R)] + C[ln(R)]3
https://www.digikey.com/en/articles/quickly-create-an-accurate-thermistor-based-temperature-sensing-circuit

## Slide 6: Analog vs. Digital
Analog
Typically a current (4–20 mA) or voltage (0–3.3 V)
Often proportional to quantity of interest: e.g., T = (100 ºC/3.3 V)*Voltage
Can be other equations: famous one in oceanography is Steinhart–Hart Equation
Digital
Sending bits (0s and 1s) and bytes (8 consecutive bits) with already translated information
01101010 = ???
Parallel vs. serial communications

## Slide 7: Binary Two possible values: 0 or 1
Paul Revere: “One if by land, and two if by sea.”
How many lanterns lit —> code for possibilities of attack
Two lanterns means 22 = 4 possibilities
  00 = Brits not coming
  01 or 10 = coming by land
  11 = coming by sea
  (Sometimes we don’t use all available permutations)
https://chaddsfordhistorical.wordpress.com/2015/07/25/mythbuster-friday-one-if-by-land-two-if-by-sea/

## Slide 8: Binary Two possible values: 0 or 1
Braille letters use six raised or unraised bumps
This gives 26 = 64 possibilities
100000 —> a

## Slide 9: What if we’re using a microcontroller
HIGH = 1
LOW = 1
That’s good for one or two bits; what if we want to transmit large numbers?

## Slide 10: Particle Argon “pinout”
If we want to transmit an 8-bit value…
28 = 256
Value could range from 0–255 inclusive

## Slide 11: What if we want to transmit large numbers? Option 1: parallel
Example: we have a temperature sensor and we want to send digital data from it to our microcontroller
Pick 8 pins
Simultaneously send your 0s and 1s on each of the 8 pins of the thermometer to each of the corresponding 8 pins on the MCU (microcontroller unit)
Thermometer

## Slide 12: What if we want to transmit large numbers? Option 1: parallel
Example: we have a temperature sensor and we want to send digital data from it to our microcontroller
Pick 8 pins
Simultaneously send your 0s and 1s on each of the 8 pins of the thermometer to each of the corresponding 8 pins on the MCU (microcontroller unit)
Very inconvenient: lots of wires, lots of parallel processing
Thermometer

## Slide 13: Option 2: Serial
Use one wire and pulse it up (1/HIGH/True) and down (0/LOW/False)
1 ≈ 3.3 V; 0 ≈ 0 V

## Slide 14: Option 2: Serial
MAJOR (POTENTIAL) PROBLEM: how do we know how many consecutive 0s or 1s we have?
I.e., the code above is 11010001. But how do we know it’s not 1111001100000011?

## Slide 15: Option 2: Serial
SOLUTION: use a second wire to send a clock (just regularly alternating 0s and 1s)
https://itp.nyu.edu/physcomp/lessons/synchronous-serial-communication-the-basics/

## Slide 16: Serial wins, but different flavors
SPI: Serial peripheral interface
I2C: Inter-inter communications
UART: Universal asynchronous receive/transmit
  TTL, RS232
SDI-12

## Slide 17: Serial wins, but different flavors
SPI: Serial peripheral interface
I2C: Inter-inter communications
UART: Universal asynchronous receive/transmit
99% of people you work with in sensor applications will just refer to all of this (and more) as serial comms
In our work, we’ll use soldered/breadboarded wires
Could also use an RS-232 cable, RS-485 cable, Ethernet cable, …
These protocols have additional details that we won’t cover this semester, but look up if you need them for your device (or interest or job)!

## Slide 18: Serial: two more challenges 1. What if we want two-way comms?
Use one serial data in (SDI) wire
One serial data out (SDO) wire

## Slide 19: Serial: two more challenges 2. What if we want multiple sensors connected?
Use multiple “chip select” (“CS”) wires but same data in/data
Note that same SDO and SDI lines go to all three peripherals
https://itp.nyu.edu/physcomp/lessons/synchronous-serial-communication-the-basics/

## Slide 20: Digital (serial) comms gives us a bunch of 0s and 1s: what next?
Datasheet for chip will tell us how to interpret the bits and bytes
Computer/electrical engineers and people with lots of patience can write code to interpret these values
In this class, we’ll use “drivers”—prepackaged code chunks—to do the interpretation

## Slide 21: Particle Argon “pinout”
Tells us what pins can be used for what functions
Sometimes multiples of a single function
  SCL/SDA vs. SCL1/SDA1 means there are two I2C ports
Sometimes one pin can have multiple functions (we tell microcontroller what to use in firmware)

## Slide 22: Analog vs. Digital
Analog
Typically a current (4–20 mA) or voltage (0–3.3 V)
Often proportional to quantity of interest: e.g., T = (100 ºC/3.3 V)*Voltage
Can be other equations: famous one in oceanography is Steinhart–Hart Equation
Good for sending “raw” voltages, instantly usable
Bad if noise could mess up reading
Digital
Sending bits (0s and 1s) and bytes (8 consecutive bits) with already translated information
01101010 = ???
Parallel vs. serial communications
Good for preventing data loss
Challenging because needs additional wires and (slightly) more complicated code/drivers

## Slide 23: Combining the two: analog + digital
ADC: Analog-to-Digital Converter
Takes an analog voltage referenced to something and converts it to a digital number that can be recorded by the microcontroller
Recorded in ADC “counts” based on resolution of microcontroller
E.g., 12-bit ADC —> 212 = 4096 possible values
We have to convert this back to the actual voltage!
Scales proportionately: V = Vref/4096*ADCcounts
Vref is fixed property of your microcontroller (3.3 V for us)
ADCcounts is what your microcontroller recorded

## Slide 24: A final plea
Until recently, it was extremely common to see SPI wires described as MISO and MOSI. Now PICO and POCI are catching on; use these terms. See more here: https://www.sparkfun.com/spi_signal_names.
Similar for “main” vs. “master” in Git(Hub) branches.